## Slide 1: Distributed SDN Control: Survey, Taxonomy, and Challenges: Section 4-6
By: Jordan Donovan

## Slide 2: Logical Classification of Distributed SDN Control Plane Architecture
Logically centralized SDN control
  Onix and SMaRtLight
  Hyperflow and Ravana
  ONOS and OpenDayLight
  B4 and SWAN
Logically distributed SDN control
  DISCO and D-SDN
  SDX-Based Controllers
Notes: Logically centralized SDN control
Onix and SMaRtLight (both use state replication for controller state redundancy)
  Onix is for large production networks and provides several tools
    Simple general-purpose API
    Central network information base abstraction
    Standard state distribution primitives for easing implementation of network applications
  Onix is beneficial in providing
    Programmatic framework for the flexible development of control applications with tradeoffs between performance and state consistency
  SMaRtLight is a fault-tolerant logically-centralized Master-Slave SDN controller platform where a single controller is in charge of all network decisions
    It contains replicas for this main controller for fault-tolerance that are kept consistent with a shared data store managed by an implementation of Replicated State Machine
    Is mostly used for small to medium-sized networks for fault-tolerance, consistency, and acceptable performance levels
Hyperflow and Ravana (both use event replication for state redundancy)
  Hyperflow is an extension of NOX into a distributed event-based control plane. Each NOX-based controller manages a subset of OpenFlow network switches
    It uses an event-propagation publish/subscribe mechanism for maintaining the global-wide network view
    Hyperflow requires minor modifications to applications, is eventually consistent, and favors availability
  Ravana is a fault-tolerant platform that not only ensures controller state but also switch state consistency
    Event-processing cycle is handled as a transaction that follows strict properties
    Follows Replicated State Machine approach but includes switch state consistency on top of it
    Performance suffers some due to the guarantee of correctness for a logically centralized controller
    If this correctness is relaxed significant performance improvements can be had
ONOS and OpenDayLight (both offer community-driven, open-source frameworks and provide full functionalities of Network Operating Systems)
  ONOS is targeted toward scalability, high availability, and performance including high level Northbound abstraction (global network view and application intent framework), supporting multiple protocols, and offering state dissemination mechanisms similar to Onix and Hyperflow to achieve consistency.
    Offers consistentMap tool and eventually consistent map tool allowing different levels of consistency
    The eventually consistent method uses optimistic replication based on gossip-based anti-entropy protocol
    The strong consistency method uses RAFT (using an elected leader controller)
  OpenDayLight is a generic and general purpose framework made to accommodate a wide variety of applications and use cases in different domains
    Main focus was to accelerate integration of SDN into legacy network environments
    Latest releases of ODL offer distributed SDN controller architecture with strong consistency using RAFT
B4 and SWAN
  Google’s B4 uses logical centralization to deploy traffic engineering (TE) as well as shortest-path routing for increase network efficiency and performance
    The main task of the TE server is to optimize bandwidth among competing applications
    Is is assumed that there is a specific consistency model used by the SDN gateway, but little information has been given on this
  SWAN is Microsoft’s intr-domain software-driven WAN deployment that also uses TE in conjunction with logical centralization to improve efficiency, reliability, and fairness of their inter-DC WAN
    Not much information has been given on this, much like Google’s B4
Logically Distributed SDN control will help with controlling heterogenous networks involving multiple autonomous systems under different administrative authorities
Disco and D-SDN
  Disco operates in a multi-domain, heterogenous environments (specifically WAN and overlay networks)
    Biggest contribution is the separation between intra-domain and inter-domain features of the control plane
      Intra-domain modules involve the main functions of the controller
      Inter-domain modules involve message oriented communication between neighbor domain controllers
    Main advantage is to adapt it to large scales networks with different ASes such as the Internet
    There are some drawbacks to Disco
      Static non-evolving decomposition of the network into several independent entities
      Network performance optimization leads to local optima instead of global optimum
      In Disco one controller is in charge of one domain but ASes may be too large for one controller
      Disco does not provide appropriate reliability strategies given its geographically distributed architecture
  D-SDN is similar
    uses main controllers and secondary controllers where the secondary serve as backup to the main. This addresses Disco’s reliability shortfalls
    Enhanced security and fault protection compared with Disco
SDX-based controllers involve deploying SDN at internet exchange points (IXP’s) which gives rise to Software Defined Exchanges (SDX’s)
  Connects participants of different domains via a shared software-based platform
  Usually aimed at bringing innovation to traditional peering as well as easing the implementation of customized peering policies and enhancing the control over inter-domain traffic management
  Consists of a smart SDX controller handling both the policy compiler and the router server
  Suffers from, same as Disco, localized optima instead of global optimum, but some work has been done to centralize the routing control plane
  They also face reliability and security concerns. There may be more vulnerabilities and resiliency such as backups should be addresse

## Slide 3: Summary and Future Perspectives
Scalability
Reliability
Consistency
Interoperability
Monitoring
Security
Other challenges
Notes: Scalability
Problems
  These concerns stem from decoupling of control and data planes as well as the the centralization of control logic in a software-based controller
  As a network grows in size the centralized SDN controller becomes overloaded
  As the network scales upwards communication delays between SDN controller and network switches may become high
Solutions
  Extend responsibilities of control layer (takes modifications to OpenFlow switches)
  Model control plane to mitigate scalability limitations (by a physically distributed control model, hierarchical control plane recommended)
  Consistency needs to be considered as strong consistency could introduce new scalability issues
Reliability
Problems
  Decoupling of control and data planes
  In a centralized control plane, failure of the central controller could collapse network
Solutions
  Logically centralized but physically distributed architecture alleviates issue
  Control state redundancy and controller failover must be considered
  Control state redundancy
    State Machine Replication orders the events and updates the network concurrently, thus several machines contain a replica of the control state
    Another option is primary and backup controllers the primary is updated, and the backups are updated periodically
  Fault Tolerance
    Master – slave (primary and backup)
    Distributed where each is updated concurrently
Consistency
Distributed SDN controller platforms are affected most by this issue
CAP theorem claims it is generally impossible to simultaneously achieve consistency, high availability, and partition tolerance
Strong consistency in distributed SDN controllers results in latencies and overhead in the form of data access which can affect network availability and scalability
Eventual or weak consistency allows higher network availability but could cause inconsistent or incorrect application behavior
Overall, achieving consistency involves a tradeoff between policy enforcement and network performance
This article suggests a hybrid approach to these tradeoffs using dynamic consistency model selection
Interoperability
This applies to not only with legacy systems but also with disparate distributed SDN controllers
There is a lack of open standards for inter-controller communications
There are several barriers for the development of these standards
Monitoring
Network monitoring is needed to develop control and management applications in distributed SDN-based networks
There are trade-offs between network monitoring and data accuracy
Security
Having distributed SDN control leads to some security improvements and some new security concerns

## Slide 4: Conclusion
Increase in SDN built on promises on the separation of concerns between network control logic and forwarding devices as well as the logical centralization of network intelligence
Physically centralized control architectures raised scalability and reliability concerns
This article looked at the existing SDN controller platforms
Scalability, reliability, consistency and interoperability are among the key competing challenges
This article suggests using the proposed SDN controller platforms and aggregating, merging, and learning from them to come to a common standard
Lastly, they propose more research and splitting of problem into two sub-areas
  Controller placement
  Knowledge sharing